## Slide 1
Changes to the Standards covering Fire Detection & Emergency Lighting
Notes: A note about the FSA.
The Fire and Security Association is a specialist group of the ECA primary focused on those who design, install, commission, maintain and monitor fire detection, emergency and Security systems. All ECA members who are third party assessed in these particular areas of work are eligible to associate themselves with both ECA and FSA membership.

## Slide 2
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Electrical Contractors’ Association.
Central Essex & Colchester Technical Forum.
E: steve.martin@eca.co.uk
T: 020 7313 4807
M: 07866 487593
@ecastevemartin
Shaping our industry
Enabling business growth
Getting members specified

## Slide 3
The Electrical Contractors’ Association
Shaping our industry
Enabling business growth
Getting members specified
Notes: A little about the ECA...

## Slide 4
The Electrical Contractors’ Association
Shaping our industry
Enabling business growth
Getting members specified
Notes: The ECA has been the driving force in the electrical engineering and building service industry since 1901
Creating many organisations which today are involved in improving industry standards
These are the result of ECA’s direct involvement and commitment in Shaping our industry, enabling business growth and getting
members specified..

## Slide 5
The Electrical Contractors’ Association
Shaping our industry
Enabling business growth
Getting members specified
Notes: Representing not just electrical contracting but the whole electrical, electro-technical and building service sectors.

## Slide 6
The Electrical Contractors’ Association
Shaping our industry
Enabling business growth
Getting members specified
Notes: We pride ourselves in being an industry specific resource offering essential information, business support, knowledge and representation to members – more than certification alone..

## Slide 7
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Electrical Contractors’ Association.
Welcome..
New BS 5266-1: 2016 – Emergency Lighting CoP
DPC of BS 5839-1 Fire alarm CoP.
Periodic Electrical Inspections – Expectations and
Frustrations
Shaping our industry
Enabling business growth
Getting members specified

## Slide 8
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
What's new...?
New BS 5266-1: 2016 – Emergency Lighting CoP
Final draft before DPC of BS 5839-1 Fire alarm CoP.
Periodic Electrical Inspections – Expectations and Frustrations
BS 5266-1:2016 Emergency Lighting

## Slide 9
Any questions..?
Legislation and Enforcement ...
Codes of Practices (BS and BS EN Standards)
BS5839, BS 5266 etc..
The Electricity at Work Regulations 1989
The Health & Safety at Work etc Act 1974
UK Regulatory Framework
LAW
Reasonably accepted / deemed to achieve conformity with the LAW
Fire and Emergency Lighting Systems (Non domestic)
The Regulatory Reform (Fire) Safety Order 2005

## Slide 10
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
The Electrical Contractors’ Association
BS 5266-1:2016 Emergency Lighting
...Give guidance on the factors to be considered when designing, installing and wiring emergency lighting..
BS 5266-1 previously concentrated
on getting people out of a building in
the event of mains failure.
Now – considers people who wish to
remain in a building and/or continue
normal operations.

## Slide 11
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Key considerations..
BS 5266-1:2016 Emergency Lighting
Major change – not just an amendment..
Increased from 44 pages to 73.
Now 13 sections with 13 annexes.
New definitions and considerations.
Came into effect 30th May 2016.

## Slide 12
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Key considerations..
BS 5266-1:2016 Emergency Lighting
Terms and Definitions (Part 3)...
This has increased from 12 to 18 items - New definitions are:
Borrowed Light – from a reliable source
Competent person – Relevant training, experience and tools
Emergency safety lighting – for those staying in the building
High risk task area lighting – potential dangerous process
Open area lighting – to avoid panic..
Sign height – Geometric shape or height.

## Slide 13
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Key considerations..
BS 5266-1:2016 Emergency Lighting
Consultation (Part 4)...
Early consultation with clients and relevant stakeholders is
key to define the way in which a system is intended to
operate.
Additional considerations is necessary if a ‘stay put’ strategy
is agreed.
An assessment of risk to the occupants of the building must
be made and a plan of action formed..

## Slide 14
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
New areas...
NEW
NEW
BS 5266-1:2016 Emergency Lighting

## Slide 15
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
High Risk Task Areas...
New requirement for High Risk Task Areas...
...If emergency escape lighting is required to provide illumination for the safety of people involved in a potentially dangerous process or situation, and to enable proper shut – down procedures for the safety of the operator and other occupants, the illuminance value should be not less than 10% of the average of the normal lighting at the location of the point of risk...
BS 5266-1:2016 Emergency Lighting

## Slide 16
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Escape route signs should be located and operated in accordance with:
BS 5499-4:2013 – For appropriate direction (Table 1)
BS EN ISO 7010:2012+A5 – Use of E001 and E002
New section regarding the maximum viewing
distance and sign height using BS 5499-4:2013,
Tables 2&3.
Escape route / safety signs..
BS 5266-1:2016 Emergency Lighting

## Slide 17
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Emergency Safety Lighting
A new section related to emergency safety lighting:
...The minimum illuminance over the area where people might have to move during a failure of the supply to the normal lighting should be not less than
1 lx on the floor area...
Considerations for:
Rooms where occupants are able to ‘stay put’.
Scenarios where it is impractical to evacuate during a supply
failure (such as hotels) but to ensure 1 hour emergency light
for evacuations is maintained.
BS 5266-1:2016 Emergency Lighting

## Slide 18
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Other Key Considerations..
Essential spares and consumables should be kept onsite to reduce
the time taken to repair a system.
If an original completion certificate is not available an inspection of the
installation should take place and if satisfactory a verification certificate
issued.
BS 5266-1:2016 Emergency Lighting
A new Small Installation Completion Certificate is available

## Slide 19
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Routine Inspection & Test.
BS 5266-1:2016 Emergency Lighting
A new section (12) setting out the requirements for routine inspections and tests:
Requires inspections and testing at regular intervals in
accordance with BS EN 50172.
Functional operation should be checked at least once a
month.
Full rated test should be performed annually.
Visual inspection of each luminaire annually.
Precautions and actions are included when testing with
particular regards to functionality after testing. (Auto Test)

## Slide 20
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Other Key Considerations..
BS 5266-1:2016 Emergency Lighting
Test facilities:
The test facility should facilitate both
monthly short tests and annual full
duration tests.
The test facility should be protected
from unauthorised operation.
The test device should not interrupt
other electrical equipment that could
cause a hazard.

## Slide 21
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Other Key Considerations..
BS 5266-1:2016 Emergency Lighting
A new requirement regarding the certification of installations:
If an installation is modified the existing log book and
documentation should be integrated into the revised
documents.
If an original completion certificate is not available an
inspection of the installation should take place and if
satisfactory a verification certificate issued.

## Slide 22
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
What's new...?
Service Standard for Fire safety systems & security
systems.
New BS 5266-1: 2016 – Emergency Lighting CoP
Final draft before DPC of BS 5839-1 Fire alarm CoP.
Revision of PD6662 – Scheme for Intruder & hold-up
alarms.
Final draft before DPC – BS 5839-1

## Slide 23
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
Draft for public comment (DPC) – Ends March 2017
New revised standard due July 2017.
Final draft before DPC – BS 5839-1

## Slide 24
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
DPC – BS 5839-1
Scope... BS 5839-1 provides recommendations for the planning, design, installation, commissioning and maintenance of fire detection and fire alarm systems in and around buildings, other than domestic premises.
BS 5839-6 has not changed

## Slide 25
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
A potentially new class of false alarm
Unwanted fire alarm signals
Environmental false alarm
Good Intent
DPC – BS 5839-1

## Slide 26
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
False Alarms – Recording the right details:
Identity and location of the device
Category of false alarm.
Reason fro false alarm
Activity in the area (if the reason for the false alarm is unknown)
Action taken on the cause of the false alarm
Whether the FRS were called
Whether the FRS attended
The person responsible for recording the information
DPC – BS 5839-1

## Slide 27
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
The possible introduction of multi-sensor detectors.
Should be used in smoke detector mode on escape routes
Must comply with EN54-7 standard.
DPC – BS 5839-1

## Slide 28
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
Previously it was a variation
Potentially now written into the standard
Hinged covers over Type A manual call points..
DPC – BS 5839-1

## Slide 29
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
A final exit must go to a place of ultimate safety.
This includes roller shutter doors or similar exits
Clarification on sighting of Manual Call Points
DPC – BS 5839-1

## Slide 30
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
Visual Alarm Devices (VADs)
Better practical guidance.
Incorporating CP001 working group with FSA input and
BRE research.
DPC – BS 5839-1

## Slide 31
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
An insight to the proposed changes..
Does this need to be double pole..?
No
But you will need to ensure you ensure safe isolation
procedures and tools.
Must be protected by unaithorised persons – key switch.
DPC – BS 5839-1

## Slide 32
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
What's new...?
New BS 5266-1: 2016 – Emergency Lighting CoP
Final draft before DPC of BS 5839-1 Fire alarm CoP.
Periodic Electrical Inspections – Expectations and Frustrations
Periodic Inspections of Electrical Systems.

## Slide 33
Rules and regulations for the prevention of fire risk arising from electric lighting - 1882
Periodic Inspections of Electrical Systems.

## Slide 34
Any questions..?
Periodic Inspections of Electrical Systems.
Necessity for periodic inspection & testing.
Legislation requires that electrical installations are maintained in a safe
condition.
The following bodies may require periodic inspection and testing:
Licensing authorities.
Public bodies.
Insurance companies.
Mortgage lenders.

## Slide 35
Any questions..?
Periodic Inspections of Electrical Systems.
What does the Legislation say..?
Electricity at Work Regulation - Regulation 4 (2) requires:
‘All systems shall be maintained so as to prevent, so far as is reasonably practicable, such danger.’
Regulation 16 – Persons to be competent to prevent danger and injury.
‘No person shall be engaged in any work activity where technical knowledge or experience is necessary to prevent danger or injury...unless under such degree of supervision..’

## Slide 36
Any questions..?
The Memorandum of guidance on the Electricity at Work Regulations 1989. – HSR25.
There is no specific requirement to carry out maintenance activity as such – what is required is that the system be kept in a safe condition..
Legislation.. The Electricity at Work Regulations 1989.
Periodic Inspections of Electrical Systems.

## Slide 37
Any questions..?
What does BS7671 say...?
Periodic Inspections of Electrical Systems.
Remember - BS 7671 is non-statutory – however compliance is generally accepted to satisfy the statutory requirements and may be used in a court of Law. (Refer to 114.1 in BS 7671).
134.2.2 - The designer of the installation shall make a recommendation for the interval to the first periodic inspection and test..
Chapter 34 – An assessment shall be made of the frequency and quality of maintenance the installation can reasonably be expected to receive during its intended life.

## Slide 38
Any questions..?
What does BS7671 say...?
Periodic Inspections of Electrical Systems.
In essence.. Periodic Inspection and Testing is a recognised method for demonstrating maintenance, as it involves assessing:
Safety.
Age.
Damage.
Corrosion and external influences.
Overloading.
Wear and tear.
Environment.
Suitability for continued use.

## Slide 39
Any questions..?
Guidance Notes 3 – Inspection & Testing
Periodic Inspections of Electrical Systems.
Table 3.2.
Sound engineering judgement should be
applied when deciding upon intervals
between inspecting and testing.
Table 3.2 may be used as a suitable starting
point.
The intervals between future inspections may
be increased or decreased as a result of the
inspection and test (Note 8).

## Slide 40
Any questions..?
The reality....
Periodic Inspections of Electrical Systems.
Privately owned dwelling:
Difficult to persuade a homeowner the benefits of periodic
inspection and testing.
It is presumed the occupier will notice any breakages or
excessive wear and arrange for precautions to be taken and
repairs carried out.

## Slide 41
Any questions..?
The reality....
Periodic Inspections of Electrical Systems.
Commercial and Industrial Installations:
Compliance is essential with The Electricity at Work
Regulations 1989.
Formal arrangements are required for maintenance, interim
routine checks and periodic inspections.
Frequency of checks and inspections will depend on the
nature of the premises and may increase with age.

## Slide 42
Any questions..?
The reality....
Periodic Inspections of Electrical Systems.
 | Legislation | Requires Electrical checks
England | Landlord and Tenant Act 1985 | No
Wales | Landlord and Tenant Act 1985 (Renting Homes Act 2016) | No (Yes?)
Northern Ireland | Private Tenancies Order (Review – Department for Social Development) | No ?
Scotland | Housing (Scotland) Act 2014 | Yes
Private Rented Sector..

## Slide 43
Any questions..?
The reality....
Periodic Inspections of Electrical Systems.
Private Rented Sector (PRS)..
Both the Electricity at Work and the
Landlord and Tenancy Act require electrical
installations to be effectively maintained.
UK Government recently committed to
introducing new powers to set requirements
for electrical safety within the PRS.

## Slide 44
Any questions..?
The Private Rented Sector....Recommendations
Periodic Inspections of Electrical Systems.
5 years
5 years
Used between change of Tenancy

## Slide 45
Any questions..?
Advice for Landlords and Tenants...
www.electricalsafetyfirst.org.uk/guides-and-advice

## Slide 46
Any questions..?
Houses of Multiple Occupancy (HMO)
Periodic Inspections of Electrical Systems.
The Management of Houses of Multiple Occupation (England) Regulation 2006 requires:
Electrical Installations to be inspected and Tested every 5 years.
A written report (Condition report).
Carried out by a suitably qualified person.
Enforced by licensing procedures.

## Slide 47
Any questions..?
Social Housing...
Periodic Inspections of Electrical Systems.
Social Housing – 5 or 10 years?
The ultimate decision is with the competent person – the
inspector.
Apply sound engineering judgment – base the decision on fact.
Maintenance regimes / programmed work may form part of the
decision.
Justification may be sought.

## Slide 48
Any questions..?
Periodic Inspections of Electrical Systems.
These are often the areas where you need help.
One persons C2 is another’s C3!
Its the competent persons judgement call – but it must be
substantiate with fact.
Good practice - assigned with a regulation number against the
coded item.
Anything written down needs to be clear and understood by
the client.
Coding – often the problem..

## Slide 49
Any questions..?
Periodic Inspections of Electrical Systems.
Coding – often the problem..
Best Practice Guide 4.
Free to download.
Industry agreed guidance.
A good reference if challenged.

## Slide 50
Any questions..?
Periodic Inspections of Electrical Systems.
Coding – above all..
Bear in mind, what we tell our members..
Over zealous with coding might lead to later criticism if your
client spent money on unnecessary remedial work.
Being to lenient with coding could have a consequence if later
something goes wrong.
Document as much as you can – keep to the contract.

## Slide 51
Internet of Things?
The Electrical Contractor’ Association
Unlocking the potential for electricians..
Electrical Contractors’ Association.
Central Essex & Colchester Technical Forum.
E: steve.martin@eca.co.uk
T: 020 7313 4807
M: 07866 487593
@ecastevemartin
Shaping our industry
Enabling business growth
Getting members specified